## Slide 1: Using Digital Image Processing and Computer Vision to Detect Brain Tumors in MRI Slices
Sean Webster
Computer Vision
4/19/2016

## Slide 2: Introduction
MRI scans completed
One whole brain takes roughly 60 scans, each about 2mm apart
  No time to look at all scans, must do every third scan (20 scans)
The Setting

## Slide 3: Introduction cont.
Tumors all have different densities. Some are denser than surrounding regions, some less dense
Tumors have complex shapes, and are not always simply connected regions
There is the possibility of multiple tumors
Problems Associated

## Slide 4: Calculating the Volume
First we have to know how many tumors there are
Is the tumor simply connected?
How will the tumor be marked by the radiologist?
Challenges

## Slide 5: Calculating the Volume
Look for the marked region(s)
  Let’s assume the region is marked in a color value not used elsewhere in the image - this allows us to easily differentiate between outside the marked region and inside
Check for closed regions of marking color– these are where our tumors are
We can now discard the rest of the image, and send each tumor to it’s own image
Approach: Finding the Marked Regions

## Slide 6: Calculating the Volume
Tumor is usually much brighter than surroundings in MRI – we can use this and threshold the image
This thresholding allows us to see the tumor better
This thresholding allows us to get better edges in edge detection, such as Sobel
Thee edges give us our regions of tumor vs non-tumor
Finding the tumor in the marked region

## Slide 7: Calculating the Volume
A region is connected if two regions on any slice are touching
A tumor is continuous if it is within 10% of size of the previous image – a continuous tumor then becomes a stack of images to simulate the 3D tumor
If regions are connected in the same image, the two tumor image stacks will be merged into one image
Checking for connected regions

## Slide 8: Calculating the Volume
Since we know each dimension of the tumor in the x-y plane of each image, we can extrapolate the shape of the tumor between images using the volume integral
  We know the thickness between each image
  We can find a mathematical function using digital boundary segmentation of our lines that we found earlier to satisfy the shape of the 2D tumor image
  Therefore we have all necessary information for 3D integral
Calculating the volume

## Slide 9: Let’s take it a step further…
What if the program finds the tumor first?

## Slide 10: Approach
Detect brain inside of skull in each slide and remove all image material that is not brain
Detect tumors per layer
Cross reference with library of other brain tumors to determine % chance of tumor

## Slide 11: Step 1: Detecting the Brain
Challenges
The shape of the brain changes for each height
Brain is not uniform color or uniform shape
Eyes and sinus cavities can be hard to differentiate from brain
Every brain is different
Tumors can distort the shape of the brain

## Slide 12: Step 1: Detecting the Brain
Different Shapes for Different Heights

## Slide 13: Step 1: Detecting the Brain
The skull is a large, dense, thick outer perimeter of our heads – very easy to detect
Use Sobel edge detection to detect skull using gradient
Thresholding allows us to push this line to 255
We now know where the skull is, but we don’t need it, or anything outside of it, so by marking where it is, we can remove it from our original image – we now only have the interior of the skull
Approach 1: Detecting the skull

## Slide 14: Step 1: Detecting the Brain
Without the skull, we are left with the brain, the eyes, the sinuses, the mouth, and the ear canals
Good news, everyone! The mouth, sinuses, and ear canals are mostly hollow, and show up black in MRI’s – we can threshold them out of our image easily!
Singling out the brain

## Slide 15: Step 1: Detecting the Brain
Eyes

## Slide 16: Step 1: Detecting the Brain
Eyes present the biggest challenge – they’re roughly tumor shape and density
Usually there is a gap between them and the brain, though.
By detecting the lines between the eyes and the brain, and histogramming each side of the line, we can tell the side with a higher concentration of gray is the brain side – we can now get rid of the eyes, and only have the brain
Eyes

## Slide 17: Step 1: Detecting the Brain
In between the skull and the brain is fluid and a membrane in the subarachnoid space – This is essentially an empty space in MRIs
By utilizing this space, we can use Sobel edge detection to separate the brain from the not brain
  This slide was written before we got to morphology – we can see that erosion followed by dilation would get rid of the skull
Note: This approach may not work when the scans get to the eyes
Approach 2: Detecting the brain directly

## Slide 18: Step 2: Detecting Tumors
Tumors rarely have uniform density/shape
Tumors are not usually the same shape/size, or in the same place – though they can be
Challenges

## Slide 19: Step 2: Detecting Tumors
Tumors show up as different color than the rest of the brain in MRIs – we can use this in image processing
We want to create high contrast, to make the tumor stick out – our tumor will hopefully be the brightest area
We can now remove everything except the tumor by thresholding
We can now use the before mentioned volume calculation method
Approach

## Slide 20: Step 3: Deep Learning
By teaching the program the location, colors, and sizes of tumors using training data, we can improve it’s understanding of these things
Once we have the training data input, we can then use linear discrimination analysis to try and find correlations between tumors
If a correlation is found, the program is ready for testing data
Calculation chance of object being a tumor